## Slide 1
[CHAPTER]
[TOPIC]
Header 1
Header 2
Header 3
Body
Note
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.

## Slide 2
DESIGN OVERVIEW
MECHANICAL
Objectives:
Strong enough to sustain weight
Easy to transport and use
Large enough size to comfortably use
Optimized for weight and volume
Electronics are secured and protected
Cost-effective solution
Protected from the harsh lunar environment
Use for 15-30 years.
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – E.A.S.E

## Slide 3
DESIGN OVERVIEW
MECHANICAL
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.
Metric | Weight | Single Panel | Single Fold Accordion
Use with EDS | 10 | 9 | 5
Robustness | 30 | 25 | 20
Weight and Volume | 20 | 20 | 12
Storage, transportation, deployment | 20 | 20 | 12
Life Cycle | 20 | 20 | 16
Total | 100 | 94 | 65

## Slide 4
DESIGN OVERVIEW
MECHANICAL
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.
Spikes for security
Electronics Box
Handle

## Slide 5
PANEL COMPOSITION
MECHANICAL
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – E.A.S.E
Beta Cloth
Alumina Ceramic Sheet
Kapton film
Kapton film
Alumina Ceramic Sheet
Lotus Coating
Electrodes
0.00762 cm
0.0032 cm
0.0032 cm
0.005 cm
0.005 cm
0.0227 cm
iPhone X
0.77 cm
EDS Panel
0.035 cm
Mass estimate: 1.36 kg

## Slide 6
MECHANICAL
MATERIAL SELECTION
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – E.A.S.E.
 | Alumina Ceramic | Bolt | Beta-cloth | Kapton
Density | 3.9 (g/cm3) | 8.0 (g/cm3) | 2.71 (10-3 g/cm2) | 1.41 (g/cm3)
Tensile Strength | 260 (MPa) | 482 (MPa) | 3,450 (MPa) | 230 (MPa)
Flexural Strength | 379 (MPa) | 290 (MPa) | 13.4 (MPa) | 120 (MPa)
Compressive Strength | 2,600 (MPa) | 170 (MPa) | 758 (MPa) | 172 (MPa)
Coefficient of Thermal Expansion | 8.6 (10-6/ºC) | 10.3 (10-6/ºC) | 9.3 (10-5/ºC) | 8.1 (10-5/ºC)
Dielectric Constant | 9.1 (at 1 MHz) | - | - | 5.42 (at MHz)
Dielectric Strength | 16.7 (kV/mm) | - | - | 217 (kV/mm)
Temperature Range | -273.15 – 1,750 (ºC) | -252 – 871 (ºC) | -73 – 260 (ºC) | -267 – 398 (ºC)
Note: we will also put LOTUS coating on the top layer of the alumina sheet and use Cicoil wires

## Slide 7
MECHANICAL
MATERIAL SELECTION
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – E.A.S.E.
 | Alumina Ceramic | Bolt | Beta-cloth | Kapton
Density | 3.9 (g/cm3) | 8.0 (g/cm3) | 2.71 (10-3 g/cm2) | 1.41 (g/cm3)
Tensile Strength | 260 (MPa) | 482 (MPa) | 3,450 (MPa) | 230 (MPa)
Flexural Strength | 379 (MPa) | 290 (MPa) | 13.4 (MPa) | 120 (MPa)
Compressive Strength | 2,600 (MPa) | 170 (MPa) | 758 (MPa) | 172 (MPa)
Coefficient of Thermal Expansion | 8.6 (10-6/ºC) | 10.3 (10-6/ºC) | 9.3 (10-5/ºC) | 8.1 (10-5/ºC)
Dielectric Constant | 9.1 (at 1 MHz) | - | - | 5.42 (at MHz)
Dielectric Strength | 16.7 (kV/mm) | - | - | 217 (kV/mm)
Temperature Range | -273.15 – 1,750 (ºC) | -252 – 871 (ºC) | -73 – 260 (ºC) | -267 – 398 (ºC)
Note: we will also put LOTUS coating on the top layer of the alumina sheet and use Cicoil wires

## Slide 8
MECHANICAL
MATERIAL SELECTION
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – E.A.S.E.
 | Alumina Ceramic | Bolt | Beta-cloth | Kapton
Density | 3.9 (g/cm3) | 8.0 (g/cm3) | 2.71 (10-3 g/cm2) | 1.41 (g/cm3)
Tensile Strength | 260 (MPa) | 482 (MPa) | 3,450 (MPa) | 230 (MPa)
Flexural Strength | 379 (MPa) | 290 (MPa) | 13.4 (MPa) | 120 (MPa)
Compressive Strength | 2,600 (MPa) | 170 (MPa) | 758 (MPa) | 172 (MPa)
Coefficient of Thermal Expansion | 8.6 (10-6/ºC) | 10.3 (10-6/ºC) | 9.3 (10-5/ºC) | 8.1 (10-5/ºC)
Dielectric Constant | 9.1 (at 1 MHz) | - | - | 5.42 (at MHz)
Dielectric Strength | 16.7 (kV/mm) | - | - | 217 (kV/mm)
Temperature Range | -273.15 – 1,750 (ºC) | -252 – 871 (ºC) | -73 – 260 (ºC) | -267 – 398 (ºC)
Note: we will also put LOTUS coating on the top layer of the alumina sheet and use Cicoil wires

## Slide 9
MECHANICAL
MATERIAL SELECTION
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – E.A.S.E.
 | Alumina Ceramic | Bolt | Beta-cloth | Kapton
Density | 3.9 (g/cm3) | 8.0 (g/cm3) | 2.71 (10-3 g/cm2) | 1.41 (g/cm3)
Tensile Strength | 260 (MPa) | 482 (MPa) | 3,450 (MPa) | 230 (MPa)
Flexural Strength | 379 (MPa) | 290 (MPa) | 13.4 (MPa) | 120 (MPa)
Compressive Strength | 2,600 (MPa) | 170 (MPa) | 758 (MPa) | 172 (MPa)
Coefficient of Thermal Expansion | 8.6 (10-6/ºC) | 10.3 (10-6/ºC) | 9.3 (10-5/ºC) | 8.1 (10-5/ºC)
Dielectric Constant | 9.1 (at 1 MHz) | - | - | 5.42 (at MHz)
Dielectric Strength | 16.7 (kV/mm) | - | - | 217 (kV/mm)
Temperature Range | -273.15 – 1,750 (ºC) | -252 – 871 (ºC) | -73 – 260 (ºC) | -267 – 398 (ºC)
Note: we will also put LOTUS coating on the top layer of the alumina sheet and use Cicoil wires

## Slide 10
MANUFACTURING
MECHANICAL
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.
Top Plate:
3-axis CNC milling
  Outsource
  Order: grooves for EDS, screw holes, outer edge, countersink screw holes
  Design considerations: 0.5 mm tolerance, space for Kapton, large external fillets
Bottom Plate:
3-axis CNC milling
  Order: grooves for EDS, screw holes, tapping screw holes, outer edge
  Design considerations: 0.5 mm tolerance, space for Kapton, large external fillets

## Slide 11
MANUFACTURING
MECHANICAL
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.
Electronics Box:
Tungsten inert gas welding:
  Weld the sidewalls of the electronics box together
3-axis CNC milling:
  Order: drill holes for mounting electronics on box, drill holes for mounting lid to box
Manually tap holds
Design considerations: 0.5 mm tolerance, large external and internal fillets