## Slide 1
CONCEPT OF OPERATIONS
Astronaut should ensure the surface is relatively flat and cleared
Astronaut lays out E.A.S.E in front of the lunar habitat and connects it to power source
After moonwalk and sample collection, astronaut returns to stand on E.A.S.E, which senses the weight and begins attracting dust off the astronauts’ boots and moving it to the center and the left and right edges
Astronaut leaves. E.A.S.E waits for another astronaut for two minutes, after which it self-cleans for several minutes, removing the dust from its surface by pushing it off its right edge, before entering standby mode until the pressure sensor is activated again.
1
2
3
4

## Slide 2
RISK ASSESSMENT CHART
  Impact of radiation and cold temp on electronics:
    The likelihood of single particle upsets is very low
    MLI (multi-layered insulation) should protect the electronics from cold temperatures
  EDS field not strong enough to clean all the way up the boots
    EDS geometry and electronics are easily altered to increase the field strength
  Abrasion of surface, materials or electrodes due to long-term use
    Ceramic has high abrasion resistance
RISK MITIGATION STRATEGIES:

## Slide 3
RISK ASSESSMENT CHART
  Dust penetration between layers
    Kapton is being compressed between two ceramic panels and acts as a gasket
  Concentrated force application onto E.A.S.E. by rocks on the surface of the moon
    Not a problem if astronauts clear the area
  Wear on bottom of E.A.S.E., as well as moving out of position:
    The spikes on the bottom of E.A.S.E secure it to the surface, limiting slipping and abrasion by loose particles underneath it
RISK MITIGATION STRATEGIES CONT’D: