## Slide 1
HOMES
Habitat Orientable & Modular Electrodynamic Shield
E100 Progress Report – 4/9/21
Professor: Dr. Soon-Jo Chung
Notes: Malcolm

## Slide 2
ADMIN
Agenda
4/9/21
Malcolm
Facilities and Funding Announcement – 2 mins
Gantt Chart Overview – 10 mins
Feedback form – 2 min
Progress reports – 40 mins
Next steps – 6 mins

## Slide 3
ADMIN
Gantt Overview
4/9/21
Malcolm

## Slide 4
ELECTRICAL
WORK PLAN
04/09/21
Amrita Mayavaram
 | EDS Design | Power Supply | Microcontroller
4/2 - 4/8 | Design & order test boards | Implement CDR feedback Design PCB | Get familiar with arduino
4/9 - 4/15 | Contact companies for custom connectors Revise large PCB design Create test plan | Bootstrap circuitry Order PCB | Program phases
4/16 - 4/22 | Soldering/Help with tests Continue design work | Space grade components | Help with tests Operational mode programming
4/23 - 4/29 | Design and order PCB for single panel prototype | Modify design and order new PCB if needed | Operational mode programming
4/30 - 5/6 | Contact rigid flex PCB manufacturers | Space grade components | Operational mode programming
5/7 - 5/13 | Soldering/Help with tests | Modify design based on tests | Soldering/ Help with tests
5/14 - 5/20 | Writing | Writing | Writing
5/21 - 5/27 | Revise designs based on test results Order rigid flex PCB | Modify design and order PCB | Look into more advanced controls
5/28 - 6/3 | Finalize and order additional components | Finalize and order additional components | Controls design
IMPORTANT TARGET DATES
4/24 – Informal Design Review
4/30 – Order Deadline for Mid-Project Report Prototype
5/10 – Complete Assembly of Electronics for MPR Prototype
5/30 – Order Deadline for End-of-Term Prototype

## Slide 5
ELECTRICAL
BUDGET
04/09/21
Amrita Mayavaram
EDS Design |  | Power Supply |  | Microcontroller | 
Item | Price | Item | Price | Item | Price
Test Boards | $250 | Earth Prototype Components | $1,000 | Arduino | $25
HV Wire | $30 | Test PCB | $100 | Breadboard | $10
Rigid PCBs | $400 | 2nd Test PCB + Components | $1,100 |  | 
Rigid Flex PCBs | $1,000 | Breadboard (wood) | $20 |  | 
Connectors | $1,000 | Space Grade Components | $5,000 |  | 
Acrylic Conformal Coating | $25 | Space Grade PCB | $300 |  | 
Subtotal | $2,705 |  | $7,520 |  | $35
 |  |  |  | TOTAL | $10,260

## Slide 6
ELECTRICAL
EDS DESIGN
04/09/21
Amrita Mayavaram, Hope Arnett, Jules Pénot
Test Board 1
Test Board 2

## Slide 7
Electrical
Power Supply and Switching
Technical Updates
Received advice from James Phillips regarding circuit
  In its current state, the MOSFETs would fail
  Recommends bootstrap circuitry for switching high voltages, which I am reading up on to put in the circuit.
Circuit Board for Electronics – Discussed how to design it (KiCAD), standards for doing so (IPC-2221), and safety working with high voltage. Still need to implement bootstrap circuitry to finish design
04/09/21
Kemal Pulungan

## Slide 8
Electrical
Power Supply and Switching
Work Plan
4-9 to 4-16: Finishing bootstrap circuitry and PCB design
4-16 to 4-23,30: Overseeing construction of the first board (will not be in-person)
Afterwards up to mid-May: Testing of electronics
Budget
Around $1000, maximum $2000 for one electronics box
Current list below, still subject to changes from James’s recommendations:
  https://docs.google.com/document/d/1OB4kSlLJixkQM1dVFev7hlX4f0RqRDF6c5C8Sh-qFfM/edit
04/09/21
Kemal Pulungan

## Slide 9
Electrical
EDS and Power Supply
Figured out a way to develop fast and automatic EDS test PCBs using KiCAD and Python and advised the EDS team on future steps
Met the Power SubSystem team and discussed design considerations and safety
Developed a High Voltage PCB Best Practices & Safety Presentation (maybe present it next time?)
Next week: bootstrapping circuit (todo help design), discuss the arcing problem for the EDS board
04/09/21
Sorina Lupu
KiCAD board EDS with 3 electrodes

## Slide 10
ELECTRICAL
ARDUINO WORK
Accomplished tasks
downloaded Arduino software
read through descriptions of basic Arduino functions (digitalWrite, pinMode) and overlap functions with C++ (if, do...while, etc.)
very basic outline of phase transition circuit
04/09/21
Raha Riazati
Arduino digital output only goes up to 5 V? analogWrite?
How much delay?

## Slide 11
ELECTRICAL
Schedule, Next Steps, Budget
04/09/21
Raha Riazati
Schedule
Week 2 – Continue to program phase transitions
Week 3-5 – Operational mode programming involving the LED
Week 6-7 – Test design and optimize further
Week 8-10 - Implement more advanced designs/controls if desired
Budget
Little to no cost given many team members have an Arduino (need to figure out which one)
Next Steps
Learn more about phase transition mechanism (timing, voltage, etc.) to incorporate into design

## Slide 12
Validation
Schedule (Structural)
Budget = $0
Need – confirmation of which materials (and thicknesses) will be possible to manufacture (Mechanical Team)
Need – maximum thicknesses for the top plate, possibility of adding metal plate under bottom panel (Electrical Team)
4/9/21
Nathan, Luis

## Slide 13
Validation
Structural Tests/Sims
Planned structural tests
Whole Panel Tests
  Three-point bend
  Cantilever
Multiple Panel Tests
  Dual Panel Three-point bend
  Dual Panel Cantilever
Finger Joint Tests (sanity check)
Link
Loads (shown in red) are 486 N total
Fixed points shown in green
4/9/21
Luis, Nathan

## Slide 14
Validation
Simulations
Simulation Timeline and Objectives
O1: Create a robust and flexible model that can represent the dynamic electric fields in HOMES. The model should further validate results from other simulations and be open to changing various parameters to optimize in later steps.
04/08/21
Isabella Dula, Sarah Yun
Week: | Goal:
1 (Current status) | Researched methodology and identified key references; higher level code design; created documentation framework
2 | Define spatial-temporal domain, boundary conditions, initial conditions, physical parameters, and iteration structure; write out pseudocode and begin preliminary scripting; meet with an expert?
3 | Write out code; begin debugging and testing to meet O1
Next Steps: Talk to electronics team to determine which parameters are best to be considered for optimization. This could include modifying voltage, particle tracing, top plate thickness, electrode spacing, and electrode width

## Slide 15
Validation
Simulations
Physics and the Finite Difference Time Domain Method
04/08/21
Isabella Dula, Sarah Yun
Physical domain
dx
dt
Boundary Conditions
Electrodes modeled as perfect electrical conductors (E-field = 0)
Implement 2nd Order Absorbing Boundary Conditions at ‘edges’ of physical domain
Iteration Structure
-Define Parameters/structures: dx, dt, total dimensions, spatially-dependent properties
-Initialize electric field based on charge of electrodes
-for i in time domain
-Update time dependent state of electrodes
-Apply electrodynamic iteration equation:
-Reinforce boundary conditions
-end
-Data visualization
Many thanks to this resource: https://eecs.wsu.edu/~schneidj/ufdtd/

## Slide 16
Validation
Simulations
Code
Considering either C or Python for the simulations
  The book we referenced used C for FDTD simulations
  Maybe C would have more flexibility since we can define our own data types with specific elements for each type?
  However, Python may be easier to read, use, debug
Could represent physical aspects of HOMES in code as objects and give relevant attributes to the object
  Ex) a node class with position, charge density, electric field, and etc as attributes
    Represent the individual nodes on the grid
  Already have some python code with various physical parts set up as classes
  Create classes for various parts of HOMES
Represent grid as matrix
  Array of arrays
04/08/21
Isabella Dula, Sarah Yun

## Slide 17
Validation
Comsol
Comsol Objectives:
Validate results from Python simulations
Trace particles to optimize design
Introduce 3rd dimension to examine interactions between panels
Combine circuitry, magnetic, thermal, etc… into Multiphysics simulation for final validation
4/9/21
Malcolm
 | Sub-task
Week 1 (4/4 - 4/10) | Set up COMSOL
Week 2 (4/11 - 4/17) | Evaluate current 2D design for field strength and capacitance
Week 3 (4/18 - 4/24) | Implement particle tracing in 2D
Week 4 (4/25 - 5/1) MIDTERMS | Optimize partical locomotion on single panel in 2D
Week 5 (5/2 - 5/8) MIDTERMS | Evaluate current 3D design for field strength, capacitance, and inductance
Week 6 (5/9 - 5/15) | Implement particle tracing in 3D
Week 7 (5/16 - 5/22) MID PROJECT REVIEW | Examine particle tracing across multiple panels in 3D
Week 8 (5/23 - 5/29) | Optimize particle locomotion across panels in 3D
Week 9 (5/30 - 6/5) | Full multiphysics 3D simulation with circuit components
Week 10 (6/6 - 6/12) FINALS | BUFFER
Next Steps:
Debrief learning with Jules and Amrita.
Determine high priority simulations with electronics team.
Crack on

## Slide 18
Validation
Comsol
4/9/21
Malcolm
Workflow
Select study type
Select domain type
Define parameters
Define geometry
Define regions
Define boundaries
Apply physics properties to corresponding domains and boundaries
Apply materials to domains
Generate mesh
Compute study
Evaluate results / post-process
Parameter sweep

## Slide 19
MECHANICAL
Bottom Plate Manufacturing and Drawings
Technical Progress:
  Reached out and got quotes for the bottom plate design
  Scheduled meetings with several Macor manufacturers
  Main issue with design is the 1mm thickness of the bottom lip on the plate
    Have to increase the thickness to at least 3mm
    The weight of the panel will increase by ~350 grams
    Will not affect the price of manufacturing
  Top sheet issue:
    1mm too thin, will warp or crack during shipping
    Tape casting as possible solution
      Mateus makes 4.5x4.5 in plates of desired thickness
  Action Items:
    Set up meeting with Ceramic Products
    Communicate with Mateus to see if we can increase the tape casting size
    Update drawings with correct bottom plate thickness
    Choose manufacturer and start ordering!!!
4/9/21
Leah Soldner

## Slide 20
MECHANICAL
Bottom Plate Manufacturing and Drawings
Budget/Timeline:
  Precision Ceramics: Mateus Truon, meeting Thursday (4/8)
    1 plate: $1756.20
    8 plates: $ 1080.50
    Delivery time: 5-7 weeks
  Morgan Advanced Materials: Nikhil Jani, meeting Wednesday (4/7)
    1 plate: $2220.22
    8 plates: $1843.03
    Delivery time: 8 weeks
  Ceramic Products: Mark Vidaic, meeting next week TBD
    1 plate: $1450
    8 plates: $1100
    Delivery Time: 4-5 weeks
  If we go with cheapest, estimated budget/timeline: $9,500/5 weeks
  If we go with most expensive, estimated budget/timeline: $15,000/8 weeks
4/9/21
Leah Soldner

## Slide 21
MECHANICAL
Panel Materials
Schedule
Week 2 – Reached out to Professor Faber about Macor and Potential Silicon use, awaiting response
Week 3 – Decide on manufacturers and place orders
Week 8 – Earliest Macor comes in, start panel assembly
04/09/21
Athena Kolli
Budget
~$2,000 per macor panel
$200 for adhesive
$?? Alumina (have to find the quote)
$?? Finger Joints
Next Steps:
Decide on use of Silicon
What will finger joints be made of? Get quote
Order materials

## Slide 22
MECHANICAL
Testing Assembly
04/09/21
Athena Kolli
Schedule
Week 2 – Determine action items for testing assembly
Week 4 – Begin writing procedures for panel assembly
Week 5 – Design 3D print for initial panel testing with PCB
Week 7 - Begin testing PCB with 3D printed panel
Next Steps:
Write panel assembly procedure
Talk to Malcolm/verification team to clarify my role

## Slide 23
MECHANICAL
ELECTRICAL ENCLOSURE DESIGN
State of the art:
Electronics enclosures serve to shield sensitive components from the space environment
A common structural material for electronics enclosures is 6061-T651 aluminum
  Fastened with screws and shear pins
  Typical enclosure weighs about 4 kg
Potting of electronics to resist shock and vibration (need to research more about this)
Passive thermal management
  Surface finishes: solar reflectors (quartz, aluminized Teflon), white paint (ex: Z98), black paint (3M Black Velvet), aluminized Kapton, metallic finishes
    Aluminum has decent IR IR absorptivity and emissivity already
    Consider black paint inside electronics box for temperature control inside
  Inserts: MLI, Aerogel, Kapton, Beta cloth
    CubeSats tend to use MLI
Active thermal management
  Louvers (vents) (maybe??)
  Pumps (this is too much for us)
04/09/21
Polina Verkhovodova, Tanmay Gupta,
Kristine Chelakkat

## Slide 24
MECHANICAL
ELECTRICAL BOX DESIGN
Thermal Control System Design process:
04/09/21
Polina Verkhovodova
STEP 1: Determine design requirements and constraints
STEP 2: Determine thermal environment
STEP 3: Identify challenges and problem areas
STEP 4: Identify applicable thermal control techniques
STEP 5: Determine radiator and heat requirements
STEP 6: Determine thermal control system mass and power

## Slide 25
MECHANICAL
ELECTRICAL BOX DESIGN
Electronics Enclosure design requirements (high level):
Shield to keep sufficient internal charging rate
Ground structural elements
Conductive path for circuitry
Thermal protection (consider extreme temperature range and thermal cycling)
Vibration tolerance
UV and ionizing radiation
Need to confirm components for lunar model (not earth-based prototype). Will use these to determine temperature ranges.
Usually, the component with the tightest temperature tolerance is the power supply. A power supply typically has an operational temperature range of 0 to 15 °C and a survival temperature range of -10 to 25 °C.
04/09/21
Polina Verkhovodova

## Slide 26
MECHANICAL
ELECTRICAL BOX DESIGN
Lunar conditions summary (work in progress):
04/09/21
Polina Verkhovodova
Temperature Range [°C] | -232 to 110
Geometric Albedo | 0.07
Orbit-Average IR [W/m^2] | 430
Values from Space Mission Analysis and Design textbook
Still looking for information regarding conditions at the south pole specifically

## Slide 27
MECHANICAL
ELECTRICAL BOX DESIGN
UV radiation
In general, aluminum is resistant to UV radiation
Not too big of a concern
Corrosion (WIP)
Corrosion is a concern! Some studies show that metals exposed to radiation are more susceptible to corrosion
Types of coatings to mitigate this:
  Barrier coatings
  Conversion coatings
  Sacrificial coatings
04/09/21
Polina Verkhovodova

## Slide 28
MECHANICAL
CABLE DESIGN AND PROTECTION
Specifications
Wire:
  4 cables
  High Voltage, 3000V
  Shielded
    Helps reduce electromagnetic and radio frequency interference from other devices
    Important due to high voltage and proximity to other electrical components
  Insulating outer coating
Connectors:
  Able to keep dust out
04/09/21
Kristine Chelakkat

## Slide 29
MECHANICAL
CABLE DESIGN AND PROTECTION
Cicoil
  Approved by NASA for space flight; Used in Apollo
  Up to 12-20kV DC (depending on gauge size)
  Shielding: 90% nominal coverage
  Temperature Rating: -104C to +165C
  Outer Jacker Dielectric Strength: 450 volts/mil
  Comes with connectors attached
04/09/21
Kristine Chelakkat

## Slide 30
MECHANICAL
CABLE DESIGN AND PROTECTION
Gore
  Previously used in space missions like Apollo and Mars Rover, and many other satellite missions
  No information about connectors – may have to manually add
04/09/21
Kristine Chelakkat

## Slide 31
MECHANICAL
CABLE DESIGN AND PROTECTION
Next Steps
Contacting engineers with HV experience in the space industry
Contacting suppliers for samples
  <$20/foot from Cicoil
  May be able to request Gore for a free sample
Testing Cable
04/09/21
Kristine Chelakkat

## Slide 32
Mechanical
Electronics Box Insulation
Aerogel
Most likely in conjunction with MLI (see Polina’s slides)
Lightweight, great insulator
Need something beyond just reflecting heat
Enhances heat retention inside box
Procurement: Caltech MS labs, JPL extras, NASA license
Already used in spaceflight
carbon-based or silica or metal oxides (outgassing?)
Thin film aerogel by NASA is promising
NASA Link
04/09/21
Tanmay & Polina

## Slide 33
Mechanical
Electronics Box Touch Sensor
Astronaut Touch Controls
Button could get “clogged” by dust
adds a point of dust ingress and point of failure
Use a touch based alternative
3 alternatives: Capacitive sensor, Piezoelectric Transducer, Strain Gauge
Piezoelectric Transducer
Best option given enclosure
generate signal/voltage change based on pressure
Adjust sensitivity to require reasonable astronaut tap pressure
Coupled with LED for status information
Already used in rockets
Cost-effective
04/09/21
Tanmay Gupta

## Slide 34
VERIFICATION
Schedule & Progress
Additional Links
Quotes: https://docs.google.com/document/d/1JMS6xeg2GfDGNQWzqpF8xgkdXztxX7Pl_0HX3a9pVhU/edit?usp=sharing
Detailed 10 Week Schedule: https://docs.google.com/document/d/1fI2mnGXqogZx00UyyNW2b-N-qA4sxLObzkvph_nNB3M/edit?usp=sharing
04/09/21
Calle Junker, Kaila Coimbra, Sydney Richardson, Parul Singh
Summarized Schedule
Week 2 and 3
  Determine parts for all tests
  Receive quotes for outsourcing tests (see link)
  Finalize all rig designs
Week 4
  Begin construction of all rigs (LTE, abrasion, glove box)
By Week 7, all rigs should be constructed and ready
We will be conducting benchtop testing when prototypes are complete

## Slide 35
VERIFICATION
Benchtop Testing
Schedule
Week 2 – Determine necessary parts and budget
Week 3 – Place order for all needed parts
Week 5 – Begin electronic benchtop testing
Week 10 - Begin mechanical benchtop testing
04/09/21
Calle Junker
Budget
$200 for oscilloscope, EMF detector, etc.
$800 for mechanical benchtop testing
  $600 for LN2, dewar, and safety equipment
  $200 for impact testing, loading
Estimated $1000 total

## Slide 36
VERIFICATION
Glovebox
Additional Info:
https://docs.google.com/spreadsheets/d/1eCWXm6SFHYvjiBSH6nSlmXVNTzdUf-_WXcTQ4h48kic/edit?usp=sharing
https://docs.google.com/document/d/1U8Kxp_ktJtrzEqrkx59jmgzuCbHyqj02b4jm5AmzpwA/edit?usp=sharing
04/09/21
Calle Junker
Budget
Estimated budget approximately $2000
  See spreadsheet in additional info for detailed breakdown of part costs (does not include nitrogen tank)
Schedule
Week 2 – Determine necessary parts and budget
Week 3 – Place order for all needed parts
Week 4 – Begin assembly
Week 5 – Glove box complete and ready for use
Next Steps:
Finalize attachment method with frame
Complete CAD of glove box assembly
Place order of all parts

## Slide 37
VERIFICATION
EFFECTIVENESS TESTING
Schedule
04/09/21
Rithvik
Item | Cost
Camera | $3000
Lights | $150
Aluminum Rails | $500
Connectors and Feet | $400
Grounding Hardware and Power Cords | $150
Total | $4600
Budget
Week Start Date | Tasks
2021-04-12 | Purchase Equipment
2021-04-19 | Start Building Frame
2021-04-26 | Continue Building Frame Start Writing Code to Analyze Results
2021-05-03 and Subsequent Weeks | Finish Building Frame Finish Writing Code Start Running Effectiveness Tests

## Slide 38
Verification
Thermal Fluctuation Testing
Testing Quotes
NTS
  $40,500
Grays Engineering
  TBD
Oneida
  TBD
04/09/21
Sydney
Test Outline
Testing one panel, -170℃ to +130℃, air-to-air or liquid-to-liquid, 30 exposures then start-up and shut-down electronics 15 times, 5-10 minute dwell time, 189 cycles total

## Slide 39
VERIFICATION+VALIDATION
Abrasion Rig Plans and Simulation Plans
Budget/Timeline for Abrasion Rig (assuming we have to build our own):
  Abrasion Rig Parts Needed and approximate cost:
    Motor, large wheel with rubber rim, metal frame, loading weight, abrasive dust simulant, tarp
    Main cost is the motor, all parts together should be $1500 max (prob closer to $1000)
    However this is a rough first-look estimate, will hash out details this weekend
  Timeline
    Week 2 - Finalize parts list and design for abrasion rig
    Week 3 - Get quotes/ Order parts
    Week 4 to Week 7 - Building the rig (somebody in Pasadena will have to do this as I am remote))
      This depends on when all parts come in
Note about Validation:
  Next week: Collect parameters needed for thermal sims like strength constants for varying temperatures, read about thermal cycling sims to figure out best plan
4/9/21
Parul Singh

## Slide 40
VERIFICATION
Long Term Effectiveness (LTE) Test
Additional Info:
https://docs.google.com/document/d/1si6GRTnZiIqzqADaSfvcGlQJqSmV7rVR-7y3NoNxfhg/edit?usp=sharing
04/09/21
Kaila Coimbra
Budget
Estimated budget of approximately $800 (rough upper estimate based on materials found)
Schedule
Week 2 – Determine necessary parts
Week 3 – Place order for all needed parts and finish LTE rig design
Week 4 – Begin assembly
Week 5/6 - Finish assembly and test if operational
Week 7 – LTE rig is fully constructed and ready for use
Next Steps:
Finalize budget
Complete CAD of LTE rig
Place order of all parts

## Slide 41
Admin / Documentation
Mid-Project Report
Proposed Timeline for Report
April 22nd - outline report sections and sync up with main content creators
May 6th - internal deadline: first draft of report (feedback from team members)
May 10th - internal deadline: second draft of final report (feedback from external advisors)
May 17th - internal deadline: post feedback revisions
May 17th-May 20th: editing, formatting and visual design of the report
May 20th – External deadline (NASA): mid-project report due
04/09/21
Helen Wexler

## Slide 42
Summary
Action Items
To Do
Complete Survey
Fill in Gantt Chart for your Task
ORDERS ORDERS ORDERS
Sub-team Meetings and Technical Work
Upload Week 3 Slides
04/09/21
Helen Wexler