## Slide 1
MECHANICAL
CABLE DESIGN AND PROTECTION
Specifications
Wire:
  4 cables
  High Voltage, 3000V
  Shielded
    Helps reduce electromagnetic and radio frequency interference from other devices
    Important due to high voltage and proximity to other electrical components
  Insulating outer coating
Connectors:
  Able to keep dust out
04/09/21
Kristine Chelakkat

## Slide 2
MECHANICAL
CABLE DESIGN AND PROTECTION
Cicoil
  Approved by NASA for space flight; Used in Apollo
  Up to 12-20kV DC (depending on gauge size)
  Shielding: 90% nominal coverage
  Temperature Rating: -104C to +165C
  Outer Jacker Dielectric Strength: 450 volts/mil
  Comes with connectors attached
04/09/21
Kristine Chelakkat

## Slide 3
MECHANICAL
CABLE DESIGN AND PROTECTION
Gore
  Previously used in space missions like Apollo and Mars Rover, and many other satellite missions
  No information about connectors – may have to manually add
04/09/21
Kristine Chelakkat

## Slide 4
MECHANICAL
CABLE DESIGN AND PROTECTION
Next Steps
Contacting engineers with HV experience in the space industry
Contacting suppliers for samples
  <$20/foot from Cicoil
  May be able to request Gore for a free sample
Testing Cable
04/09/21
Kristine Chelakkat