## Slide 1
MECHANICAL
ELECTRICAL ENCLOSURE DESIGN
State of the art:
Electronics enclosures serve to shield sensitive components from the space environment
A common structural material for electronics enclosures is 6061-T651 aluminum
  Fastened with screws and shear pins
  Typical enclosure weighs about 4 kg
Potting of electronics to resist shock and vibration (need to research more about this)
Passive thermal management
  Surface finishes: solar reflectors (quartz, aluminized Teflon), white paint (ex: Z98), black paint (3M Black Velvet), aluminized Kapton, metallic finishes
    Aluminum has decent IR IR absorptivity and emissivity already
    Consider black paint inside electronics box for temperature control inside
  Inserts: MLI, Aerogel, Kapton, Beta cloth
    CubeSats tend to use MLI
Active thermal management
  Louvers (vents) (maybe??)
  Pumps (this is too much for us)
04/09/21
Polina Verkhovodova, Tanmay Gupta,
Kristine Chelakkat

## Slide 2
MECHANICAL
ELECTRICAL BOX DESIGN
Thermal Control System Design process:
04/09/21
Polina Verkhovodova
STEP 1: Determine design requirements and constraints
STEP 2: Determine thermal environment
STEP 3: Identify challenges and problem areas
STEP 4: Identify applicable thermal control techniques
STEP 5: Determine radiator and heat requirements
STEP 6: Determine thermal control system mass and power

## Slide 3
MECHANICAL
ELECTRICAL BOX DESIGN
Electronics Enclosure design requirements (high level):
Shield to keep sufficient internal charging rate
Ground structural elements
Conductive path for circuitry
Thermal protection (consider extreme temperature range and thermal cycling)
Vibration tolerance
UV and ionizing radiation
Need to confirm components for lunar model (not earth-based prototype). Will use these to determine temperature ranges.
Usually, the component with the tightest temperature tolerance is the power supply. A power supply typically has an operational temperature range of 0 to 15 °C and a survival temperature range of -10 to 25 °C.
04/09/21
Polina Verkhovodova

## Slide 4
MECHANICAL
ELECTRICAL BOX DESIGN
Lunar conditions summary (work in progress):
04/09/21
Polina Verkhovodova
Temperature Range [°C] | -232 to 110
Geometric Albedo | 0.07
Orbit-Average IR [W/m^2] | 430
Values from Space Mission Analysis and Design textbook
Still looking for information regarding conditions at the south pole specifically

## Slide 5
MECHANICAL
ELECTRICAL BOX DESIGN
UV radiation
In general, aluminum is resistant to UV radiation
Not too big of a concern
Corrosion (WIP)
Corrosion is a concern! Some studies show that metals exposed to radiation are more susceptible to corrosion
Types of coatings to mitigate this:
  Barrier coatings
  Conversion coatings
  Sacrificial coatings
04/09/21
Polina Verkhovodova