## Slide 1
Validation
Structural Simulation
Luis, Nathan
4/16/21
Ran Full Assembly Compression Simulation
  Fixed bottom (flat surface)
  486 N Centered Circular Load
Dimensions: 15 x 15 cm
Top Plate: Zirconia
Bottom Plate: Macor
Elements ~ 13655
Nodes ~ 26673
Missing Constants on Data Sheets
Factor of Safety
Min - 55
Displacement
Max – 4e-4 mm

## Slide 2
Validation
Structural Simulation
Luis, Nathan
4/16/21
Ran Full Assembly “3-point bend” Simulation
  Fixed 10% of panel on opposite sides (flat surface)
  486 N Centered Circular Load
Dimensions: 15 x 15 cm
Top Plate: Zirconia
Bottom Plate: Macor
Elements ~ 43100
Nodes ~ 83089
Missing Constants on Data Sheets
Factor of Safety
Min – 2.79
Displacement
Max – 5.52e-2 mm