## Slide 1
[CHAPTER]
[TOPIC]
Header 1
Header 2
Header 3
Body
Note
AIAA Caltech Student Branch – 18/11/20
Preliminary Design Review – H.O.M.E.S.

## Slide 2
VERIFICATION
TEST PROGRAM
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – EASE
Operational Test^*†
Vibration Test for Deployment †
Mechanical Load Tests
600 N Pulsating Fatigue Test*!
Maximum Load Test*!
Sharp Impact Test Simulating Micrometeorites*!
EMI Test for EDS System^*†
Simulated Abrasion Test*
Dust Exposure Test
Goal: Validate to TRL4
Implement safety factor of 1.2 – 1.5
Miscellaneous
Abrasion Test*!
Electronic Life Test for 45 years^*
Key:
^ Under vacuum conditions
* Under thermal conditions
! Destructive test
† Full prototype needed

## Slide 3
VERIFICATION
TEST PROGRAM
Equipment and Testing Conditions
AIAA Caltech Student Branch – 11/18/20
Preliminary Design Review – EASE
(Roy, 2008)
Three-Body Abrasive Wear Test Rig
Currently looking for resources for vacuum and cryochamber
Lunar Simulant JSC-1A will be used for EDS-related testing
Lunar Simulants OB-1 and Chenobi are the most recommended simulants for abrasion and dust exposure testing
We will test from -260˚C to 140˚C to simulate lunar thermal conditions